## Slide 1: CeNSE Evacuation Procedure
2025
CeNSE-EP-01 Version 4.5
Reviewer | Approver
CeNSE EHSS Committee | Chair, CeNSE EHSS Committee
Date | 07-01-2026

## Slide 2: ERT Members
 | Primary | Backup | Responsibility (in order)
ERT 1 | Pavan Nukala | Sushobhan Avasthi | Primary incharge of all safety incident. Part of 3-man team that investigates the incident. If needed, call fire. When appropriate, declare "all-clear“
 | P: 9515393595 | P: 9902333360 | 
 | pnukala@iisc.ac.in | savasthi@iisc.ac.in | 
ERT-2 | Gajendra M | Jagadeesha KB | 
 | P: 9535550474 | P: 7795385941 | 
 | gajendram@iisc.ac.in; | Jagadeeshakb@iisc.ac.in | 
ERT-3 | Saurabh Chandorkar | Thiyaganand R | 
 | P: 7022321404 | P: 8971118917 | 
 | saurabhc@iisc.ac.in | thiyaganandr@iisc.ac.in | 
ERT-4 | Saleem Ahmed | Arjun M | Incharge of control room. Change the Magnetic board on the Exit door towards Utility building. Call ambulance/security. Collects reports from floor in-charges. Call fire, if needed
 | P: 7348922321 | P: 9496920250 | 
 | saleemb@iisc.ac.in | arjunm1.cense@vendor.iisc.ac.in | 
Assembly point | Suresha S J | Sabiha Sultana | Manage the crowd at assembly point Relay information to control room Do not let people leave Take attendance
 | P:9482773717 | P: 9591323919 | 
 | sureshasj@iisc.ac.in | sabihas@iisc.ac.in | 

## Slide 3: ERT Members
 | Primary | Backup | Responsibility (in order)
Ground Floor Leader | Nandeesh N | Sreetosh Goswami | During evacuation ensure the population to the nearest exit Report to control room if you see any unconscious people Report back to control room after evacuation Do not enter rooms that seem unsafe Do not help unconscious people
 | P: 9980201320 | P: 7044184754 | 
 | nandeeshn.cense@vendor.iisc.ac.in | sreetosh@iisc.ac.in | 
 | Rajesh R | Bindu Poornima | 
 | P: 7259631005 | P: 9008465465 | 
 | rajeshr@iisc.ac.in | binduj.cense@vendor.iisc.ac.in | 
First Floor Leaders | Akshay Naik | Usha Vijay | 
 | P: 9611396194 | P: 9902599116 | 
 | anaik@iisc.ac.in | ushavijay.cense@vendor.iisc.ac.in | 
 | Gayathri Pillai | Vini Gautam | 
 | P: 7642802806 | P: 9108687294 | 
 | gpillai@iisc.ac.in | vini@iisc.ac.in | 
Second Floor Leader | Manoj Varma | Jithin MA | 
 | P: 9902346297 | P: 7012177455 | 
 | mvarma@iisc.ac.in | jithinma@iisc.ac.in | 
 | Somashekar P S | Seema Jaiswal | 
 | P: 8762203074 | P: 7250211023 | 
 | somashekarps.cense@vendor.iisc.ac.in | seemajaiswal@iisc.ac.in | 
Third Floor Leaders | Aditya Sadhanala | Anish Itagi | 
 | P: 9606122796 | P: 7892598535 | 
 | sadhanala@iisc.ac.in | anishitagi.cense@vendor.iisc.ac.in | 
 | Supradeepa V. R. | Veera Pandi N | 
 | P: 8277155752 | P: 9739744049 | 
 | supradeepa@iisc.ac.in | veerapandi.cense@vendor.iisc.ac.in | 

## Slide 4: ERT Members
 | Primary | Backup | Responsibility (in order)
MNCF Leaders | Abhishek Chaturvedi | Dhanalakshmi | 1. Make sure MNCF evacuates 2. Report to control room
 | P: 9481940054 | P: 7348860925 | 
 | abhishekc@iisc.ac.in | pdhanalakshm.cense@vendor.iisc.ac.in | 
 | Ambresh m | Kumar MP | 
 | P: 9731883339 | P: 9886565894 | 
 | ambreshm@iisc.ac.in | kumarmp.cense@vendor.iisc.ac.in | 
NNFC Leaders | Ajeya Shettar | JAYACHANDRA REDDY | 1. Make sure NNFC evacuates 2. Report to control room
 | P: 8861817002 | P: 8792207303 | 
 | ajeyashettar@iisc.ac.in | jayachandrar@iisc.ac.in | 
 | Chandan HB | Rekha | 
 | P: 9036423944 | P:7760107913 | 
 | chandanh@iisc.ac.in | rekham@iisc.ac.in | 

## Slide 5
Evacuation procedure: During Working Hours
All information goes through control room
= BMS
= ERT 1/2/3
= ERT4
= Assembly point incharge
= Floor/NNfC/MNCF Leaders
= Assembly point
= Control room
= Accident site
Alarm
(BMS)
Report to ERT in control room
(BMS)
Note alarm location. Take over BMS computer
(BMS)
Generate list of occupants from biometric
(ERT1, 2 & 3)
Investigate. Carry walkie. Use SCUBA for plenum, SF30, 31, 32, and 33.
(ERT1, 2 & 3)
Cordon off the area. Victims? Turn-off power? Open windows?
(ERT1, 2 & 3)
Go to control room
(ERT4)
Change the Magnetic board on the Exit door towards Utility building.
(ERT4)
Set-up control room in GF09. Get brief from BMS
(ERT4)
Call security. If ERT asks, call fire truck &ambulance
(AP Incharge)
Go to the assembly point. Manage the crowd.
(AP Incharge)
Any pertinent information from crowd?
(Floor Leaders)
Evacuate your floor. Do not enter plenum, SF30, 31, 32, and 33. Just knock.
(Floor Leaders)
Report to control room.
(AP Incharge) Count the NNfC & MNCF occupants.
(AP Incharge) One reverts to control room
(ERT1, 2 & 3)
Go to control room. Get brief from BMS.
(AP Incharge) Go back & take attendance for NNfC & MNCF occupants
(ERT4)
Coordinate with ambulance/fire

## Slide 6
Evacuation procedure: During Non-Working Hours
= BMS
= ERT 1/2/3
= ERT4
= Assembly point incharge
= Floor/NNfC/MNCF Leaders
= Assembly point
= Control room
= Accident site
Alarm
(BMS)
Go to control room. Note alarm location.
(BMS)
Go to accident site. Do what you can. Call & brief ERT
(BMS)
If needed, call security, fire truck, ambulance
(ERT1, 2 & 3)
Investigate. Carry walkie. Use SCUBA for plenum, SF30, 31, 32, and 33.
(ERT1, 2 & 3)
Cordon off the area. Victims? Turn-off power? Open windows?
(ERT1, 2 & 3)
Go to control room
(ERT4)
Coordinate with ambulance/fire
(ERT1, 2 & 3)
Go to accident site. Get brief from BMS.
(BMS)
Arrange a floor-wise search using security & volunteers
ERT1 is the first faculty or senior staff on the scene.
ERT 2 is one of the BMS staff on-site.
Use help of on-site security. They can coordinate with ambulance and fire station.

## Slide 7: Actors and Actions
The Job
Respond to the emergency
Do
Take walkie-talkie from BMS
Handle the emergency as appropriate and cordon off the area
Issue all-clear
Do not
Enter hazardous rooms without SCUBA
Take decisions
The Job
Manage control room
Do
Upon evacuation, take over the control room
Interact with floor leader & assembly point incharges.
Call security, fire, ambulance
Do not
Go to incident site.
Assist security, fire, ambulance
Change the Magnetic board on the Exit door towards Utility building.
ERT 1,2,3
ERT 4
The Job:
Primary source of information.
Do:
Go to control room
Locate the incident site
Quickly call ERT 1/2/3
Hand over walkie-talkie and provide brief
Find # of occupants from biometric
Do not:
Stay in BMS room.
BMS

## Slide 8: Actors and Actions
Assembly Point In Charges
Floor/MNCF/NNfC Leaders
The Job:
Ensure population evacuates through the nearest exit
Do:
Knock on lab door to ask people to leave
Report back to control room after evacuation
Do not:
Enter rooms that seem unsafe
Help unconscious people
The Job:
Manage the crowd at assembly point
Do:
Collect pertinent information from the crowd
Count MNCF/NNfC occupants
Report to Control room with the count and information
Do not:
Let people leave
Collect attendance sheet from emergency room
Take attendance of NNfC & MNCF occupants

## Slide 9: FAQ
Posters in each bay describe the emergency evacuation procedure
Panic button clearly marked
Emergency shut down protocol of tools – one copy in BMS, one at the bay
2 BMS personnel are present at all times
  BMS personnel trained on tool emergency shutdown
In case of alarm, DO NOT wait for any confirmation or announcement. Just leave
Panic Button are to be pressed only for Facility Emergency and not for personnel emergency. Call BMS for personnel emergency

## Slide 10: Step 1: Raise the Alarm
Trigger fire alarm. Press panic button
Prioritize your safety. We don’t want two victims.
Err on the side of caution
Call at 115
Facility Emergency
Local Emergency
Fire/ Smoke
Injury
Spills

## Slide 11: Step 2: Evacuate
Take the nearest exit
Follow signs towards exit
Don’t use lifts
Hit emergency stop button
Don’t remove gown

## Slide 12: Step 2A: Additional Instruction for Tool Alarms in LPCVD/Diffusion
Call at 115 from corridor

## Slide 13: Step 2C: Power Outage
Cleanroom is on UPS backup, so power should never go out in NNfC
In case of power loss, wait for 2 mins
  Tools are designed to default to a “safe” state
  Diesel generator should come online
Else, assume a major breakdown and evacuate.

## Slide 14: Step 3: Report to Assembly Point
Go to the designated assembly point
Stay in the assembly area. We need a headcount of NNfC & MNCF occupants
Don’t go for coffee!
Dr. Suresha
Sabiha
Please obey assembly point in charges
Inform them if you have any pertinent information

## Slide 15: Overpressure Calculations
Vapor Cloud Energy (VCE, E)
  2.23x109 J= 533 kg of TNT
Ambient pressure at Bangalore (P0) is 90.1 kPa
Max overpressure at “Safe Distance” is 1 psi or 6.9 kPa
From the graph, “Scaled R” is 0.4 to 4.
Distance scales with speed of the wavefront (Mach number)
RDet = 120 m
RDef = 12 m
Pierorazio, A.J., Thomas, J.K., Baker, Q.A. and Ketchum, D.E. (2005), An update to the Baker–Strehlow–Tang vapor cloud explosion prediction methodology flame speed table. Proc. Safety Prog., 24: 59-65. https://doi.org/10.1002/prs.10048
Mach number
Detonation
Deflagration

## Slide 16: Stand in designated assembly area on the road
50 m
160 m
Assembly area
16 m
Minimal Effect
Limited structural damage
Complete destruction
Gas banks

## Slide 17: People coming from IDS building
From IDR
Normal day
During Evacuation

## Slide 18: Step 3B: Reporting during Non-Office Hours
Go to designated assembly point
Stay in assembly area. We may need a headcount
Don’t go for coffee!
Inform BMS + security
Inform Tool FT/SFT/TM
Message on the User group

## Slide 19: Step 4: Wait for an “All-Clear”
Only the emergency response team (ERT 1, 2, or 3) can give an “all-clear”
Prof. Sushobhan
Prof. Pavan
Gajendra M
Prof Saurabh

## Slide 20: Emergency Response: Summary
Call BMS immediately in case of any local emergency
  Remember 115.
  If 115 is not responsive, call tool owner, bay-in charge, Technology manager, COO -- in that order. Phone numbers are posted near the phone.
In facility emergency, evacuate through nearest exit,
  Press panic button if you notice fire or smoke
  Don’t wait to ungown
  Wait at the assembly points
In non-office hours
  Also inform BMS
  Call tool owner, bay-in charge, Technology manager, COO -- in that order.
  Message the user group

## Slide 21: Emergency Numbers
 | Contact | Number
IISc CeNSE | ERT Team | EPABX: 115 P: 080-23229333-24
 | Engineering | EPABX: 128/113 P: 8971118917, 9535550474, 9901011042, 7795385941
 | IISc safety control room | 080-2293 5555
 | IISc Security | 080-2293 2225
 | IISc ICU on Wheels | 080-2293 4444
 | OLSEH Office | 080-2293 3199
 | IISc Health center/Ambulance | 080-2293 2390
 | Snake Rescue Volunteer | 080 2293 2506
Outside | Yeshwanthpur fire station | 080-101, 080-2297 1544
 | Sadashivanagara police station | 080-100, 080-2294 2526
 | Ambulance | 080-102 080-108
 | Mallya Hospital | 080-2224 2325
 | M. S. Ramaiah Hospital | 080-2360 8888
 | Manipal Hospital | 080-2521 1200
 | Columbia Asia | 080-3989 8969
 | Narayana Hrudayalaya | 080-27835000-18

## Slide 22: Description Of Revision
Version | Date | Description of Change | Sections Affected | Approved By
4.4 | 2025 | Previous approved version | — | —
4.5 | 07-01-2026 | 1.Updated Emergency Response Team (ERT) members 2. “All-Clear” authority list: Thiyaganand R replaced by Prof. Saurabh | Step 4: Wait for an “All-Clear” (ERT Authorization Section) | Chair, EHSS Committee